## Slide 1: Questions

## Slide 2
1. What are the seven layers of the network reference model?

## Slide 3
5. Consider a point-to-point link 4 km in length. At what bandwidth would propagation delay (at a speed of 2x108 m/s) equal transmit delay for 100-byte packets? What about 512-byte packets?

## Slide 4
11. How “wide” is a bit on a 10-Gbps link? How long is a bit in copper wire, where the speed of propagation is 2.3x108 m/s?

## Slide 5
12. How long does it take to transmit x KB over a y-Mbps link? Give your answer as a ratio of x and y.

## Slide 6
13. Suppose a 1-Gbps point-to-point link is being set up between the Earth and a new lunar colony. The distance from the moon to the Earth is approximately 385,000 km, and data travels over the link at the speed of light-3x108 m/s.
(a) Calculate the minimum RTT for the link.
(b) Using the RTT as the delay, calculate the delay x bandwidth product for the link.

## Slide 7
(c ) What is the significance of the delay x bandwidth product computed in (b)?
(d) A camera on the lunar base takes pictures of the Earth and saves them in digital format to disk. Suppose Mission Control on Earth wishes to download the most current image, which is 25 MB. What is the minimum amount of time that will elapse between when the request for the data goes out and the transfer is finished?

## Slide 8
16. Calculate the latency (from first bit sent to last bit received) for the following:
(a) 100-Mbps Ethernet with a single store-and-forward switch in the path and a packet size of 12,000 bits. Assume that each link introduces a propagation delay of 10 us and that the switch begins retransmitting immediately after it has finished receiving the packet.

## Slide 9
(b) Same as (a) but with three switches.
(c) Same as (a), but assume the switch implements “cut-through” switching; it is able to begin retransmitting the packet after the first 200 bits have been received.

## Slide 10
19. Calculate the delay x bandwidth product for the following links. Use one-way delay, measured from first bit sent to first bit received.
(a) 100-Mbps Ethernet with a delay of 10 us.
(b) 100-Mbps Ethernet with three store-and-forward switches like that of Exercise 16(b), packet size of 12,000 bits, and 10 us per link propagation delay.

## Slide 11
(c ) 1.5-Mbps T1 link, with a transcontinental one-way delay of 50 ms.
(d) 1.5-Mbps T1 link between two ground stations communicating via a satellite in geosynchronous orbit, 35,900 km high. The only delay is speed-of-light propagation delay from Earth to the satellite and back.

## Slide 12
20. Hosts A and B are each connected to a switch S via 100-Mbps links. The propagation delay on each link is 20 us. S is a store-and-forward device; it begins retransmitting a received packet 35 us after it has finished receiving it. Calculate the total time required to transmit 10,000 bits from A to B
(a) As a single packet.
(b) As two 5000-bit packets sent one right after the other.
A
A
S
B

## Slide 13
21. Suppose a host has a 1-MB file that is to be sent to another host. The file takes 1 second of CPU time to compress 50% or 2 seconds to compress 60%.
(a) Calculate the bandwidth at which each compression option takes the same total compression + transmission time.
(b) Explain why latency does not affect your answer.

## Slide 14
22. Suppose that a certain communications protocol involves a per-packet overhead of 50 bytes for headers and framing. We send 1 million bytes of data using this protocol; however, one data byte is corrupted and the entire packet containing it is thus lost. Give the total number of overhead+loss bytes for packet data sizes of 1000, 10,000, and 20,000 bytes. Which size is optimal?

## Slide 15
24. Consider a network with a ring topology, link bandwidths of 100 Mbps, and propagation speed 2x108 m/s. What would the circumference of the loop be to exactly contain one 1500-byte packet, assuming nodes do not introduce delay? What would the circumference be if there was a node every 100m, and each node introduced 10 bits of delay?

## Slide 16
26. For the following, assume that no data compression is done, although in practice this would almost never be the case. For (a) to (c), calculate the bandwidth necessary for transmitting in real time:
(a) Video at a resolution of 640x480, 3 bytes/pixel, 30 frames/second.
(b) Video at a resolution of 160x120, 1 byte/pixel, 5 frames/second.
(c) CD-ROM music, assuming one CD holds 75 minutes’ worth and takes 650 MB.
(d) Assume a fax transmits an 8x10-inch black-and-white image at a resolution of 72 pixels per inch, 1 bit/pixel. How long would this take over a 14.4-kbps modem?

## Slide 17
29. Suppose a shared medium M offers to hosts A1, A2, …, AN in round-robin fashion an opportunity to transmit one packet; hosts that have nothing to send immediately relinquish M. How does this differ from STDM? How does network utilization of this scheme compare with STDM?

## Slide 18
30. Consider a simple protocol for transferring files over a link. After some initial negotiation, A sends data packets of size 1 KB to B; B then replies with an acknowledgment. A always waits for each ACK before sending the next data packet; this is known as stop-and-wait. Packets that are overdue are presumed lost and are retransmitted.

## Slide 19
(a) In the absence of any packet losses or duplications, explain why it is not necessary to include any “sequence number” data in the packet headers.
(b) Suppose that the link can lose occasional packets, but that packets that do arrive always arrive in the order sent. Is a 2-bit sequence number (that is, N mod 4) enough for A and B to detect and resend any lost packet? Is a 1-bit sequence number enough?
(c) Now suppose that the link can deliver out of order and that sometimes a packet can be delivered as much as 1 minute after subsequent packets. How does this change the sequence number requirements?

## Slide 20
1. Show the NRZ, Manchester, D-Manchester, and NRZI encodings for the bit pattern 1001111100010001. Assume that the NRZI signal starts out low.

## Slide 21
2. Show the 4B/5B encoding, and the resulting NRZI signal, for the following bit sequence:
1110 0101 0000 0011

## Slide 22
5. Assuming a framing protocol that uses bit stuffing, show the bit sequence transmitted over the link when the frame contains the following bit sequence:
11010111110101111110101111110
Mark the stuffed bits.

## Slide 23
6. Suppose the following sequence of bits arrives over a link: 1101011111010111110010111110110
Show the resulting frame after any stuffed bits have been removed. Indicate any errors that might have been introduced into the frame.

## Slide 24
11. Show that two-dimensional parity allows detection of all 3-bit errors.

## Slide 25
12. Give an example of a 4-bit error that would not be detected by two-dimensional parity. What is the general set of circumstances under which 4-bit errors will be undetected?

## Slide 26
13. Show that two-dimensional parity provides the receiver enough information to correct any 1-bit error (assuming the receiver knows only 1 bit is bad), but not any 2-bit error.

## Slide 27
14. Show that the Internet checksum will never be 0xFFFF (that is, the final value of sum will not be 0x0000) unless every byte in the buffer is 0. (Internet specifications in fact require that a checksum of 0x0000 be transmitted as 0xFFFF; the value 0x0000 is then reserved for an omitted checksum. Note that, in ones complement arithmetic, 0x0000 and 0xFFFF are both representations of the number 0.)

## Slide 28
18. Suppose we want to transmit the message 11100011 and protect it from errors using the CRC polynomial x3+1.
(a) Use polynomial long division to determine the message that should be transmitted.
(b) Suppose the leftmost bit of the message is inverted due to noise on the transmission link. What is the result of the receiver’s CRC calculation? How does the receiver know that an error has occurred?

## Slide 29: Hamming Code
Test if these code words are correct, assuming they were created using an even parity Hamming Code . If one is incorrect, indicate what the correct code word should have been. Also, indicate what the original data was.
  010101100011
  111110001100
  000010001010

## Slide 30
23. Consider an ARQ algorithm running over a 40-km point-to-point fiber link.
(a) Compute the one-way propagation delay for this link, assuming that the speed of light is 2x108 m/s in the fiber.
(b) Suggest a suitable timeout value for the ARQ algorithm to use.
(c) Why might it still be possible for the ARQ algorithm to time out and retransmit a frame, given this timeout value?

## Slide 31
39. What kind of problems can arise when two hosts on the same Ethernet share the same hardware address? Describe what happens and why that behavior is a problem.

## Slide 32
43. Let A and B be two stations attempting to transmit on an Ethernet. Each has a steady queue of frames ready to send; A’s frames will be numbered A1, A2, and so on, and B’s similarly. Let T=51.2us be the exponential backoff base unit.
Suppose A and B simultaneously attempt to send frame 1, collide, and happen to choose backoff times of 0xT and 1xT, respectively. Meaning A wins the race and transmits A1 while B waits.

## Slide 33
At the end of this transmission, B will attempt to retransmit B1 while A will attempt to transmit A2. These first attempts will collide, but now A backs off for either 0xT or 1xT, while B backs off for time equal to one of 0xT, …, 3xT.
(a) Give the probability that A wins this second backoff race immediately after this first collision; That is, A’s first choice of backoff time k x 51.2 is less than B’s.

## Slide 34
(b) Suppose A wins this second backoff race. A transmits A3, and when it is finished, A and B collide again as A tries to transmit A4 and B tries once more to transmit B1. Give the probability that A wins this third backoff race immediately after the first collision.
(c) Give a reasonable lower bound for the probability that A wins all the remaining backoff races.
(d) What then happens to the frame B1?
This scenario is known as the Ethernet capture effect.

## Slide 35
44. Suppose the Ethernet transmission algorithm is modified as follows: After each successful transmission attempt, a host waits one or two slot times before attempting to transmit again, and otherwise backs off the usual way.
(a) Explain why the capture effect of the previous exercise is now much less likely.
(b) Show how the strategy above can now lead to a pair of hosts capturing the Ethernet, alternating transmissions, and locking out a third.
(c) Propose an alternative approach, for example, by modifying the exponential backoff. What aspects of a station’s history might be used as parameters to the modified backoff?

## Slide 36
48. Suppose Ethernet physical addresses are chosen at random (using true random bits).
(a) What is the probability that on a 1024-host network, two addresses will be the same?
(b) What is the probability that the above event will occur on one or more of 220 networks?
(c) What is the probability that, of the 230 hosts in all the networks of (b), some pair has the same address?

## Slide 37
Hint: The calculation for (a) and (c) is a variant of that used in solving the so-called Birthday Problem: Given N people, what is the probability that two of their birthdays (addresses) will be the same? The second person has probability 1-1/365 of having a different birthday from the first, the third has probability 1-2/365 of having a different birthday from the first two, and so on. The probability that all birthdays are different is thus
(1-1/365)(1-2/365)…(1-(N-1)/365) which for smallest N is about
1-[1+2+…+(N-1)]/365

## Slide 38
53. How can a wireless node interfere with the communications of another node when the two nodes are separated by a distance greater than the transmission range of either node?

## Slide 39
54. Why is collision detection more complex in wireless networks than in wired networks such as Ethernet?

## Slide 40
55. How can hidden terminals be detected in 802.11 networks?

## Slide 41
56. Why might a wireless mesh topology be superior to a base station topology for communications in a natural disaster?

## Slide 42: 58
Network | Link Interface
200.23.16.0/21 | 0
200.23.24.0/24 | 1
200.23.20.0/24 | 2
otherwise | 3
Which interface will be used by this router for the following destination addresses?
11001000 00010111 00010110 10100001
11001000 00010111 00010100 10101010
11001000 00010111 00011100 10111110
11001000 00010111 00011000 11101010

## Slide 43: 59. Find a spanning tree